## Slide 1
Performance-Review
Date:19/06/2024
Name: Vamshi Krishna Emmadi
Evaluating Prof: Prof. Partha Saha
Department @Bajaj : CAE Power Train
Reporting Manager: Mr. Tagore Janaswamy

## Slide 2: Agenda
Problem Statement
Approach
Project Overview
Literature Survey
CNN Architectures (Methods to solve)
Data Generation
Results

## Slide 3: Problem Statement
1) Crank seal oil leaks can cause serious damage to a bike engine.
2) Checking IP67 Compliance is important factor:
To avoid oil leakages
To ensure prevention of entrance of foreign
particles which may lead to corrosion of inner parts of assembly.

## Slide 4: Problem Statement
Engine oil Seepage:

## Slide 5: Approach
2)Using Artificial Intelligence, we can predict contact pressures in minutes!!
3)We can train and use a machine learning model which can predict contact pressures for any contact surface in a much lesser time.
1)Leakage happens through zero contact pressure points, checking zero contact pressure points through CAE/FEA (Virtual testing) takes around 20 hours.
CAE - 20HOURS APPROX.
ML MODEL – 1 MIN

## Slide 6: Project Overview
Project Title:
Machine Learning based approach for predicting sealing pressure to achieve IP67 compliance
Key Deliverables:
Contact pressure prediction through machine learning algorithm for a given project application and correlation with CAE results
Input sample (image+text)
Output sample (image)
Bolt load, pitch, material, width etc..
ML MODEL

## Slide 7: Literature Survey
Extraction of Flow Features for Predicting Pressure Distribution Using Convolutional Neural Networks (CNNs):
By Prince Tyagi, Priyam Gupta and Raj Kumar Singh

## Slide 8: CNN Architectures
Image Vectors
Text Vectors
Concatenated vectors
Output Image
Image
Text
Image Encoder
Text Encoder
Encoding-Decoding Architecture:
Transpose CNN
Decoder
Encoder
Combined vectors
Inputs
output

## Slide 9: CNN Architectures
Encoding-Decoding Architecture:

## Slide 10: Data Generation
Output images
Input Images
FEA

## Slide 11: Data generation Methodology
2 bolt configuration
Bottom & top aluminum plates
NAM32 paper gasket
NAM32 properties
Contact Pressure
Displacement Animation
xp
yp
W
H
W-xp
H-yp
2 bolt configuration
W
H
yp
H-yp
xp
W-xp
4 bolt configuration
W
H
xp
yp
H-yp
W-xp
W/2
6 bolt configuration
W
H
xp
yp
H-yp
W-xp
9 bolt configuration
W/2
H/2

## Slide 12: Data Generation Input Image & Data
Sample input image
Sample output image
0.12, 6000
Sample text description
Xp/W
Bolt Load
xp
yp
W
H
W-xp
H-yp
810 input images and corresponding 810 output images and their associated text descriptions are generated.

## Slide 13: Encoding – decoding - Method

## Slide 14: Direct CNN – Image to Image (with padding loads)

## Slide 15: Masked Images - CNN

## Slide 16: Encoder-decoder(multiple layers)(Image-vector-Image)

## Slide 17: 1-encoder-multiple decoders(Image-vector-Image)

## Slide 18: Flatten()+Decoder Method
Final Result: Out of all the models, this model gave the highest accuracy that is 91.7% exactly, So we can use this model to predict contact pressures at different contacts of any 3D Model, and the points with zero contact pressure are the ones prone to leakage, so an engineer can focus on those points to ensure IP67 rating.
Conclusion:

## Slide 19
Thank You